## Slide 1: Learning Microgrid Dynamics via UDEs and Bayesian Neural ODEs
Accurate, interpretable, and calibrated models for microgrid decision-making
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17

## Slide 2: Why SciML for Microgrids?
Fast, nonlinear, mode-switching dynamics; stiff DAEs are slow, black-box learners violate physics
Goal: accurate, interpretable, calibrated surrogates for control & what-if planning
Approach: UDE (physics + learned residual) and BNODE (Bayesian Neural ODE with calibration)
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: Microgrids face fast, nonlinear, mode-switching dynamics. High-fidelity DAEs are stiff and slow; black-box models break physics and fail OOD. We use SciML: UDE keeps physics and learns the residual; BNODE learns full dynamics with calibrated uncertainty.

## Slide 3: Limits of PINNs & Pure Black-Box
PINNs: failure modes & gradient pathologies; spectral bias; stiffness challenges
Black-box: poor extrapolation; constraint violations
Structure-preserving ODEs + stiff solvers avoid these issues
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: Why not PINNs? Known failure modes (trivial minima, gradient pathologies, spectral bias) and trouble with stiffness. UDE/BNODE preserve structure and use proper ODE solvers and Bayesian inference.

## Slide 4: Two-State Microgrid Model
x₁: storage SoC with efficiency losses; x₂: frequency/power deviation
dx₂/dt = −α x₂ + β(P_gen − P_load) + γ x₁
Testbed for structure-aware learning and calibrated UQ
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: Two-state model: x1 = storage SoC with efficiency; x2 = frequency/power deviation with damping, power coupling, and storage interaction. This minimal model captures key operational behavior.

## Slide 5: UDE: Physics + Learned Residual
Learn fθ(P_gen) only; preserve storage physics
Tiny MLP (n=3; 9 params), Rosenbrock23, composite loss favoring x₂
Symbolic extraction → cubic saturation insight
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: UDE learns only f_theta(P_gen), preserving storage physics. Tiny network (n=3; 9 params), Rosenbrock23 for stiffness, composite loss focused on x2. Symbolic extraction later shows a cubic saturation.

## Slide 6: BNODE: Uncertainty-Aware Dynamics
Bayesian parameters; NUTS sampling; PPC checks
Single α_cal post-calibration for nominal coverage
Enables chance-constrained, risk-aware ops
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: BNODE places distributions over ODE parameters. We run NUTS, check R-hat/ESS, then apply a single α_cal variance scale to hit nominal coverage. Gives risk-aware predictions useful for chance constraints.

## Slide 7: Results Summary
Test set: 10 scenarios / 2010 points
UDE vs Physics (x₂ RMSE): 0.2475 vs 0.2520
Δ=-0.004488 (95% CI [-0.038517, 0.031438]), Wilcoxon p=0.9219
BNODE coverage ~ 0.541 / 0.849 (50% / 90%), NLL ↓ ~98.48% after calibration
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: Test set: 10 scenarios, 2010 points. UDE vs physics on x2 RMSE: 0.2475 vs 0.2520; Δ≈-0.004488 (95% CI [-0.038517, 0.031438]), Wilcoxon p=0.9219. BNODE calibration: 50%/90% ≈ 0.541/0.849; NLL drops ~98.48% after calibration.

## Slide 8: BNODE Reliability — Empirical vs nominal coverage (square plot)
[Missing image: None]
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: Post-calibration, reliability curves hug the diagonal. Slight over/under-confidence removed by a single global variance scale α_cal. This is actionable for risk-aware ops.

## Slide 9: Posterior Predictive Checks — Trajectories with median, 50/90% bands
[Missing image: None]
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: Posterior predictive bands cover trajectories without bias. No post-warmup divergences, good ESS — posterior seems healthy.

## Slide 10: Calibration Sweep — Coverage error & NLL vs α_cal
[Missing image: None]
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: Global α_cal ≈ 1.8 gives minimal coverage error and massive NLL improvement (268801 → 4089). One knob; big payoff.

## Slide 11: UDE Residual (Symbolic) — Cubic fit; R² ≈ 0.982
[Missing image: None]
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: UDE residual cubic fit (R²≈0.982): mild saturation as P_gen→1. Suggests adaptive droop: β(P_gen)=β0(1 - c·P_gen²), with c≈0.018945. Physically interpretable and useful for controller tuning.

## Slide 12: UDE Ablations — Width & λ sweeps
[Missing image: None]
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: UDE is stable across width and λ; width=3 suffices. Regularization trades fit vs generalization smoothly.

## Slide 13: Noise Robustness — UDE RMSE & BNODE intervals vs σ
[Missing image: None]
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: As input noise rises, UDE RMSE degrades ~linearly; BNODE widens intervals to maintain coverage — distinguishes epistemic vs aleatoric.

## Slide 14: Runtime & Deployment
Sub-ms UDE trajectories with stiff solver → real-time feasible
BNODE for planning: intervals for chance constraints
Hybrid strategy: UDE in the loop, BNODE audits
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: UDE stays fast (sub-ms per trajectory) with a stiff solver in the loop, suitable for real-time or MPC contexts.

## Slide 15: Takeaways
UDE: physics-comparable accuracy + interpretability (cubic saturation)
BNODE: calibrated UQ (single α_cal), actionable risk
Together: reliable surrogates for control & planning
Provenance: release/minimal-figures-and-analysis @ cbbaefe • generated 2025-09-17
Notes: Use UDE for real-time, physics-faithful control; use BNODE for planning under uncertainty. Together: interpretable, calibrated, and operationally ready.